## Slide 1: Computer Architecture (EE 371 / CE 321 / CS 330)
Dr. Farhan Khan
Assistant Professor,
Dhanani School of Science & Engineering,
Habib University

## Slide 2: Outline: Unit 1
Computer Architecture: The Big Picture
Defining Performance
Measuring Performance

## Slide 3: Computer Engineering: The Big Picture
Operating System
Development
Testing
Deployment / Operation
Requirements
Specification
Design
Process View
Applications
Computer Architecture
Digital Logic Circuits
Transistors/ICs
Structural View

## Slide 4: Computer Engineering: The Big Picture
Operating System
Development
Testing
Deployment / Operation
Requirements
Specification
Design
Process View
Applications
Computer Architecture
Digital Logic Circuits
Transistors/ICs
Structural View

## Slide 5
=
=
Cellphone
Workstation
Supercomputer
“Computer”: Examples

## Slide 6: “Computer”: Examples
Smart Grid
Smart Irrigation
Automotive
Avionics

## Slide 7: Computer Architecture: The Big Picture
Input
Output
Memory
Processor

## Slide 8: Computer Architecture: The Big Picture
Input
(Keyboard,
Mouse)
Output
(LCD, Printer)
Memory
Processor

## Slide 9: Computer Architecture: The Big Picture
Input
Output
Memory
Processor
Datapath
Control Unit
Control Unit:
Reads an instruction from the Memory
Interprets the instruction and generates signals that tell other components what to do

## Slide 10: Computer Architecture: The Big Picture
Input
Output
Memory
Processor
Datapath
“0”
time
Clock Cycle
Control Unit
“1”
Control Unit:
“Clock” is a signal that keeps the Control Unit moving.

## Slide 11: Computer Architecture: The Big Picture
Input
Output
Memory
Processor
Datapath
“0”
time
Clock Cycle
Control Unit
“1”
Summary:
Processor can execute instructions (such as “add two numbers” or “multiply two numbers”)
An instruction may take a certain number of clock cycles to complete

## Slide 12: Computer Architecture: The Big Picture
Input
Output
Memory
Processor
Datapath
“0”
time
“Add”
Control Unit
“1”
“Multiply”
Summary:
Processor can execute instructions (such as “add two numbers” or “multiply two numbers”)
An instruction may take a certain number of clock cycles to complete

## Slide 13: Computer Architecture: The Big Picture

## Slide 14: Defining “Performance”
When we say one computer has better performance than another, what do we mean?

## Slide 15: Defining “Performance”
Which airplane has the best performance?

## Slide 16: Defining “Performance”
Individual User
Response Time / Execution Time
  The time between start and completion of a task
Datacenter Manager
Throughput
  The total amount of work done in a given time
  For example, tasks/transactions per hour

## Slide 17: Defining “Performance”
Individual User
Response Time / Execution Time
  The time between start and completion of a task
Datacenter Manager
Throughput
  The total amount of work done in a give time
  For example, tasks/transactions per hour
We will need different performance metrics for personal mobile devices, which are more focused on response time, versus servers, which are more focused on throughput.

## Slide 18: Interplay between “Response Time” and “Throughput”

## Slide 19: Interplay between “Response Time” and Throughput

## Slide 20: Defining “Performance”
Individual User
Response Time / Execution Time
  The time between start and completion of a task
Datacenter Manager
Throughput
  The total amount of work done in a give time
  For example, tasks/transactions per hour
We will need different performance metrics for personal mobile devices, which are more focused on response time, versus servers, which are more focused on throughput.
In this course, we will primarily be concerned with
Response Time / Execution Time as a measure of Performance

## Slide 21: Defining “Performance”
Performance of a Computer X is defined in terms of the execution time of a program on Computer X:

## Slide 22: Defining “Performance”
Performance of a Computer X is defined in terms of the execution time of a program on Computer X:

## Slide 23: Defining “Performance”
Performance of a Computer X is defined in terms of the execution time of a program on Computer X:
Computer X is n times faster than Computer Y:

## Slide 24: Measuring “Execution Time”
Elapsed time
  Total response time, including all aspects
  Processing, I/O, OS overhead, idle time
  Determines system performance
CPU time
  Time spent processing a given job
  Discounts I/O time, other jobs’ shares
  Comprises user CPU time and system CPU time

## Slide 25: Defining “Performance”
Performance of a Computer X is defined in terms of the execution time of a program on Computer X:

## Slide 26: Defining “Performance”
Performance of a Computer X is defined in terms of the execution time of a program on Computer X:
In this course, we will mostly focus on CPU Performance

## Slide 27: Classical Performance Equation
Classical performance equation:

## Slide 28: Classical Performance Equation
Input
Output
Memory
Processor
Datapath
“0”
time
“Add”
Control Unit
“1”
“Multiply”

## Slide 29: Classical Performance Equation
Input
Output
Memory
Processor
Datapath
“0”
time
“Add”
Control Unit
“1”
Toy Example:
Instruction Count = 2 (1 add, 1 multiply)
Clock Cycles for Add instruction = 1
Clock Cycles for Multiply instruction = 2
CPI = (2+1)/2 = 1.5
Clock Period = 1 sec
CPU Time = Instruction Count x CPI x Clock Period
= 2 x 1.5 x 1
= 3 sec
“Multiply”

## Slide 30: Improving Performance
Input
Output
Memory
Processor
Datapath
“0”
time
“Add”
Control Unit
“1”
Toy Example:
Instruction Count = 2 (1 add, 1 multiply)
Clock Cycles for Add instruction = 1
Clock Cycles for Multiply instruction = 1
CPI = (1+1)/2 = 1
Clock Period = 1 sec
CPU Time = Instruction Count x CPI x Clock Period
= 2 x 1 x 1
= 2 sec
“Multiply”

## Slide 31: Classical Performance Equation
Classical performance equation:
These formulas are particularly useful because they separate the three key factors that affect performance.
We can use these formulas to compare two different implementations or to evaluate a design alternative if we know its impact on these three parameters.

## Slide 32: Classical Performance Equation
Classical performance equation:
Performance depends on
  Algorithm: affects IC, possibly CPI
  Programming language: affects IC, CPI
  Compiler: affects IC, CPI
  Instruction set architecture: affects IC, CPI, Tc

## Slide 33: Instruction Set
Instruction Set
  The vocabulary of instructions a computer can understand
Different Computers have different instruction sets
  But with many common aspects
Examples
  RISC-V
  MIPS
  Intel x86

## Slide 34: Categories of RISC-V Instructions
Arithmetic
Data Transfer
Logical
Shift
Conditional Branch
Unconditional Branch

## Slide 35: Arithmetic Instructions of RISC-V

## Slide 36: The Two Camps: CISC vs RISC
Complex Instruction Set Computer
Includes multi-clock complex instructions
Memory-to-memory: LOAD and STORE incorporated in instructions
Small code sizes
Transistors used for storing complex instructions
Intel x86
Example:
MULT M[5],M[3],M[2]
Reduced Instruction Set Computer
Single-clock, reduced instruction only
Register to register: "LOAD" and "STORE“ are independent instructions
Large code sizes
Spends more transistors on memory registers
RISC-V, MIPS, ARM, PowerPC
Example:
LOAD R1,M[3] LOAD R2,M[2] MUL R3,R1,R2 STORE M[5],R3

## Slide 37: CISC vs RISC
Classical performance equation:
The CISC approach attempts to minimize the number of instructions per program, sacrificing the number of cycles per instruction.
RISC does the opposite, reducing the cycles per instruction at the cost of the number of instructions per program.

## Slide 38: Example

## Slide 39: Example

## Slide 40: Example

## Slide 41: Example

## Slide 42: Example